## Slide 1
Real-Time Vibration Monitoring System
SRAVANA LEKHA KANDE

## Slide 2
jhj
CONTENTS
1
Understanding the Case Study
2
3
4
5
6
7
8
9
10
Approach to the Case Study
Architecture Overview
Design Decisions
Planning the Workflow
How I Started
Building the GUI
Signal Processing & Alerting
Integration & Testing
Challenges Encountered
Improvements
11
12
Conclusion & Takeaways

## Slide 3
1
Understanding the Case Study
Carefully read the requirements: monitor 4 accelerometer signals, display live vibration waveforms/FFTs, implement real-time alerts, and deliver a robust, practical GUI.
Realism in simulated signals: isn’t mandatory—instead, clarity, engineering judgment, and maintainability are key.
Identified core deliverables: working Python application, a clear design, and an insightful presentation.

## Slide 4
2
Approach to the Case Study
Broke the project into logical parts:
  Simulate multi-channel sensor data
  Create a responsive GUI for visualization
  Implement real-time signal processing and alerting

## Slide 5
3
Architecture Overview
Data Simulator:
Generates multi-frequency synthetic accelerometer signals.
Uses sinusoidal components plus noise for realism.
Rolling time windows to simulate continuous data stream.
GUI Frontend:
Built with PyQt5 for cross-platform desktop application.
Displays 4 independent sensor panels with waveforms and FFTs.
Threading & Data Flow:
Simulator runs in dedicated QThread to avoid blocking UI.
Data emitted via Qt signals to ensure thread-safe, asynchronous updates.
Signal Processing:
RMS, peak, and FFT computations done on incoming data.
Alerts are triggered if vibration exceeds configured thresholds.

## Slide 6
4
Design Decisions
Used PyQt5 to make separate sensor panels that each show their own plots and alerts, keeping the code organized and easy to manage.
Made sensor signals by adding together several sine waves with some noise; changed the time step each time to make the waveforms move and look real.
Ran the sensor simulator in a background thread so the program stays fast and the screen doesn’t freeze.
Updated the plots smoothly using matplotlib’s special redraw method without slowing down the app.
Set up live alerts that change on the screen when vibration goes above limits, so problems are easy to spot.

## Slide 7
5
Planning the Workflow
Selected libraries:
  PyQt5 for GUI (professional and well-supported)
  matplotlib for plotting (easy to integrate in PyQt)
  numpy for signal simulation and processing
Listed out main steps:
  Develop and test data simulation
  Prototype core sensor visualization panel
  Add multi-sensor layout and threading for live updates
  Build alert logic and user controls
  Iterate and refine for user experience

## Slide 8
6
How I Started
Began by designing and testing the accelerometer simulation.
Used a mix of sine waves and noise for each channel.
Implemented rolling time windows for dynamic, lively signals
Created small test scripts to plot waveforms and FFTs for one sensor
Confirmed signal composition looked realistic and usable

## Slide 9
7
Building the GUI
Designed a clear and organized main window that displays all four sensor panels side by side for easy comparison.
Each sensor panel is a self-contained widget showing live vibration waveforms, FFT, and key statistics like RMS, peak,values, and status with a alert based on vibration alerts.
To ensure smooth performance, the data simulation is run in a separate QThread, streaming signals continuously.
Using Qt signals and slots, the simulator's output is connected to the GUI updates safely, maintaining thread safety and responsiveness throughout the app.

## Slide 10
8
Signal Processing & Alerting
Implemented RMS and peak detection to monitor vibration intensity
Added FFT per sensor for frequency analysis—ensured multiple peaks for realism
Developed user-configurable thresholds, panel status flips to “ALERT” on exceedance

## Slide 11
Show real-time waveforms
- Show frequency spectrum (FFT)
- Display RMS and peak info
Flow Chart
Simulation
Simulate 4 Accelerometer Data Streams (multi-frequency sine waves + noise with rolling time window)
Process Data
Compute RMS
Detect Peak values
Perform FFT for each sensor
Display Data in GUI
Show real-time waveforms
Show frequency spectrum (FFT)
Display RMS, peak, and status info
Threshold Alerting
Compare RMS with user-configured limits
Update alert status on sensors
Provide User Interaction
Threshold configuration input
Pause/Resume the data stream

## Slide 12
9
Integration & Testing
Integrated all software components: the accelerometer data simulator, sensor panels with waveforms and FFTs, and the alerting system.
Connected the simulated data stream to the GUI plots using Qt signals for real-time updates.
Tuned buffer sizes and plot redraw timing to ensure smooth and continuous visualization without lag.
Tested using various simulated signal combinations and user interactions like threshold changes.
Focused on debugging threading issues and maintaining GUI responsiveness—achieved a fluid, stable user experience.

## Slide 13
Challenges Encountered
Threading & Safety: Needed to avoid direct UI updates from worker threads—solved with Qt signals and moveToThread pattern.
Live Signals: Original simulation created static, repetitive waveforms. Fixed by advancing the time base on every data window.
Responsiveness: Had to tune matplotlib redraws and buffer sizes for smoothness without blocking the interface.
Realism: Designing synthetic signals that represent plausible vibration required careful composition of amplitudes and frequencies.
10

## Slide 14
Improvements
Extend simulation to support more sensors, or shock events
Integrate with physical sensor hardware or add richer simulation scenarios
Add options for saving/exporting runs and advanced analytics
Further refine GUI layout and accessibility
Implement persistent logging for audit or field engineers
11

## Slide 15
Conclusion & Takeaways
Developed the system step-by-step: from clear case study analysis through design, prototyping, integration, and delivery
Focused on clarity, maintainability, and real-time performance
Happy to present a working solution that matches engineering and design goals
12

## Slide 16
THANK YOU
Grateful to the Archer team for providing me the opportunity to present my case study.